## Slide 1
ESP32 Wi-Fi RC Car
Integrating Web-Based Control with Real-Time Ultrasonic Obstacle Detection and Safety Systems
Course: Internet of Things
Date: May 2024

## Slide 2
Team Members
Mohamed Hamed Ibrahim
Mohamed Mohab Mohamed
Youssef Mohamed Yahya
Youssef Ossama Mohamed
Mahmoud Samir Abd El-Rahim
Omar Mohamed Gamal
Rawan Mohamed Mohamed
Hager Hagag Sayed
Nour Amin Ahmed
Rawan Waled Galal
Mariam Samir Habib

## Slide 3
Remote Connectivity
Establishing a wireless Access Point on the ESP32 to host a cross-platform web interface for real-time robotic maneuvering without the need for external mobile apps.
Autonomous Safety
Implementing an ultrasonic-based feedback loop to detect environmental barriers and trigger immediate safety stops, preventing physical damage to the robot chassis.
PROJECT OBJECTIVES

## Slide 4
Wi-Fi Access Point: The ESP32 creates its own local network, ensuring low-latency communication.
Web-Based UI: A custom HTML5 page featuring a virtual joystick for intuitive touch or mouse control.
Edge Processing: All logic—from parsing joystick coordinates to obstacle math—is performed locally on the ESP32 dual-core chip.
SYSTEM OVERVIEW

## Slide 5
Category | Component | Function
Core | ESP32 Microcontroller | Wi-Fi Server & Central Processing Unit
Actuation | L298N Motor Driver + 2 DC Motors | Dual-channel H-Bridge for directional control
Sensing | HC-SR04 Ultrasonic Sensor | Proximity and distance measurement
Security | Active Buzzer | Audible collision alert system
Power | Power Bank (USB) | Stable 5V power supply for electronics
HARDWARE COMPONENTS

## Slide 6
Control Layer
User connects to WiFi AP. Phone browser sends X/Y coordinates via HTTP requests.
Processing Layer
ESP32 parses data, calculates differential steering, and checks sensor distance.
Action Layer
L298N activates motors based on PWM; Buzzer sounds if safety limit is breached.
SYSTEM ARCHITECTURE

## Slide 7
Motor Driver (L298N): GPIO 27, 26, 18, 19 (IN1-IN4).
Ultrasonic (HC-SR04): Trig to GPIO 23, Echo to GPIO 32 via 1k/2k Divider.
Buzzer: Positive to GPIO 25, Negative to GND.
Power: Unified Ground across all modules is critical for signal stability.
WIRING & PIN CONFIGURATION
ESP32 GPIO Pin | Connected Component | Function
GPIO27, GPIO26 | L298N IN1, IN2 | Right Motor Direction Control
GPIO18, GPIO19 | L298N IN3, IN4 | Left Motor Direction Control
GPIO23 | HC-SR04 TRIG | Sends ultrasonic pulse
GPIO32 | HC-SR04 ECHO (via voltage divider) | Receives reflected signal
GPIO25 | Buzzer (+) | Obstacle alert sound
GND | All modules | Common ground
5V / VIN | HC-SR04 VCC | Sensor power

## Slide 8
Differential Steering
Rather than spinning in place, the system calculates a variable speed for each wheel based on the Joystick X-axis:
Inner Wheel: Speed decreases to act as a pivot point.
Outer Wheel: Speed increases to drive the arc of the turn.
Result: Smooth, realistic vehicle motion.
STEERING LOGIC

## Slide 9
The sensor uses high-frequency sound waves to measure distance. To protect the ESP32, a Voltage Divider (1kΩ and 2kΩ resistors) scales the 5V Echo signal down to a safe 3.3V level.
*0.034 represents the speed of sound in cm/μs.
ULTRASONIC SENSING LOGIC

## Slide 10
15
Centimeters (Threshold)
Safety Protocol
Instant Halt: If distance < 15cm, the ESP32 overrides user commands and brakes all motors.
Audible Alert: The GPIO 25 triggers the active buzzer to notify the operator.
Lockout: Forward motion remains disabled until the obstacle is cleared or the robot is reversed.
COLLISION PREVENTION

## Slide 11
Web Server
Asynchronous web server hosting HTML/JS resources directly from ESP32 Flash memory.
Main Loop
Real-time polling of distance sensor interleaved with user command execution.
SOFTWARE & CODE

## Slide 12
Source Code Highlights

## Slide 13
Source Code Highlights

## Slide 14
Source Code Highlights

## Slide 15
Source Code Highlights

## Slide 16
Robot Assembly Photos
[INSERT FINAL ASSEMBLY PHOTOS HERE]

## Slide 17
CIRCUITRY & WIRING

## Slide 18
System Demonstration
Live Testing and Functional Verification
Thank you! Questions?